## Slide 1: CE101 Engineering Drawing Lec3: ORTHOGRAPHIC PROJECTIONS
Indian Institute of Technology Guwahati
Notes: Today we will discuss about the Modeling and

## Slide 2
In engineering drawing, the word ‘projection’ means
an image or the act of obtaining the image of an object.
Technical people often refer to the image as a view.
This lecture reviews methods of projection and the important terms and the conventions associated with them.
Projection System
Observer or stationary point
Object
Projectors
Plane of projections (POP)

## Slide 3
PROJECTION METHOD
Depending on the relationship between the projectors and POP and the number of POPs used for the projections, the projection methods are classified as shown in Fig.

## Slide 4: Orthographic Projections
Orthographic Projections is a technical drawing in which different views of an object are projected on different reference planes observing perpendicular to respective reference plane.
Different Reference planes are;
  Horizontal Plane (HP)
  Vertical Plane (VP)
  Side or Profile Plane (PP)
Different views are;
  Front View (FV) – Projected on VP
  Top View (TV) – Projected on HP
  Side View (SV) – Projected on PP

## Slide 5
Types of views
Projections
Converge
Parallel
Orthogonal
Oblique
Axonometric
Multiview
Pictorial drawing
Perspective drawing
Multi-view drawing

## Slide 6
View comparison
Pictorial drawing
Perspective drawing
Multi-view drawing
Difficult to create
Easy to visualize.
Shape and angle distortion
Object looks more like what our eyes
perceive.
Size and shape distortion
Right angle becomes obtuse angle.
Circular hole becomes ellipse
Distorted
width
Accurately presents object’s details, i.e.
size and shape.
Require training
to visualization.
Advantage
Disadvantage
Type

## Slide 7
PRINCIPAL PLANES
A POP is a plane on which a particular view is projected.
In multiview orthographic projections,
  Different POPs are required to draw different views of an object.
  Three such planes, perpendicular to each other, are called principal planes or reference planes (RP).
Types of RPs
Horizontal Plane: A plane parallel to the ground (or horizon) is called horizontal plane (HP) or horizontal reference plane (HRP).
Vertical Plane: A plane perpendicular to the ground and intersecting the HP is called vertical plane (VP) or frontal reference plane (FRP).
Profile Plane: A plane perpendicular to the HP and the VP and intersecting both of them is called profile plane (PP) or profile reference plane (PRP).

## Slide 8
Front View When the observer looks at the object from the front, the view obtained is called the front view (FV) or Elevation. FV is seen on the VP.
Top View When the observer looks at the object from above, the view obtained is called top view (TV) or plan. TV is seen on the HP.
Side Views When the observer looks at the object from side, i.e., from his left-hand side or righthand side, the view obtained is called side view (SV). SV is seen on the PP.
Left-Hand Side View When the observer views the object from his left-hand side, the view obtained is called left-hand side view (LHSV).
Right Hand Side View When the observer views the object from his right-hand side, the view obtained is called as right-hand side view (RHSV).
Bottom View When the observer looks to the object from below, the view obtained is called bottom view (BV) or bottom plan.
Rear View When the observer looks to the object from back, the view obtained is called rear view (RV) or back view or rear elevation.
The FV, TV and either LHSV or RHSV are usually drawn in orthographic projection. The other views are added if they are extremely essential.

## Slide 9
Projection systems
1. First angle system
2. Third angle system
First
quadrant
Third
quadrant
- European countries - ISO standard
- Canada, USA, Japan, Thailand
Transparent
planes
Opaque
planes

## Slide 10
1st angle system
(Opaque planes)
3rd angle system
(transparent planes/glass box)
Orthographic views

## Slide 11
Folding
line
Folding
line
Folding
line
Folding
line


1st angle system
3rd angle system
Orthographic views

## Slide 12
1st angle system
3rd angle system
Front View
Front View
Right Side View
Right Side View
Top View
Top View
Views arrangement

## Slide 13
Projection symbols
1st angle system
3rd angle system
d
1.7d
2.2d

## Slide 14

A.I.P.
 to Vp
&
 to Hp

A.V.P.
 to Hp &  to Vp
PLANES
PRINCIPAL PLANES
HP AND VP
AUXILIARY PLANES
Auxiliary Vertical Plane
(A.V.P.)
Profile Plane
( P.P.)
Auxiliary Inclined Plane
(A.I.P.)

## Slide 15
THIS IS A PICTORIAL SET-UP OF ALL THREE PLANES.
ARROW DIRECTION IS A NORMAL WAY OF OBSERVING THE OBJECT.
BUT IN THIS DIRECTION ONLY VP AND A VIEW ON IT (FV) CAN BE SEEN.
THE OTHER PLANES AND VIEWS ON THOSE CAN NOT BE SEEN.
X
Y
HP IS ROTATED DOWNWARD 900
AND
BROUGHT IN THE PLANE OF VP.
PP IS ROTATED IN RIGHT SIDE 900
AND
BROUGHT IN THE PLANE OF VP.
X
Y
X
Y
VP
HP
PP
FV
ACTUAL PATTERN OF PLANES & VIEWS
OF ORTHOGRAPHIC PROJECTIONS
DRAWN IN
FIRST ANGLE METHOD OF PROJECTIONS
LSV
TV
PROCEDURE TO SOLVE ABOVE PROBLEM:-
TO MAKE THOSE PLANES ALSO VISIBLE FROM THE ARROW DIRECTION,
A) HP IS ROTATED 900 DOUNWARD
B) PP, 900 IN RIGHT SIDE DIRECTION.
THIS WAY BOTH PLANES ARE BROUGHT IN THE SAME PLANE CONTAINING VP.
PATTERN OF PLANES & VIEWS (First Angle Method)
Click to view Animation
On clicking the button if a warning comes please click YES to continue, this program is
safe for your pc.

## Slide 16
NOTATIONS
Following notations should be followed while naming
Different views in orthographic projections.
IT’S FRONT VIEW a´ a´ b´
Same system of notations should be followed
incase numbers, like 1, 2, 3 – are used.
OBJECT POINT A LINE AB
IT’S TOP VIEW a a b
IT’S SIDE VIEW a´´ a´´ b´´
TERMS ‘ABOVE’ & ‘BELOW’ WITH RESPECT TO H.P.
AND TERMS ‘INFRONT’ & ‘BEHIND’ WITH RESPECT TO V.P.

## Slide 17
Multi-view orthographic projections
In this type of projection, we imagine the object being drawn in the center of a transparent box.
The different views of the object are projected onto the sides of this box.

## Slide 18: Multi-view orthographic projections
The projection box and its six views are spread in such a way as to place all the views on the same plane.
The other views pivot around the front view.
BOTTOM VIEW
LEFT SIDE VIEW
REAR VIEW
FRONT VIEW
RIGHT SIDE VIEW
TOP VIEW

## Slide 19: Multi-view orthographic projections
Among the six possible views, we will choose to portray those necessary to the description of the shape of the object.
FRONT VIEW
RIGHT SIDE VIEW
TOP VIEW
LEFT SIDE VIEW
REAR VIEW
BOTTOM VIEW
Three views are usually enough to portray an object. Many simple objects may only require one or two views.

## Slide 20
S.V.
F.V.
V.P.
P.P.
FOR T.V.
FOR S.V.
FOR F.V.
OBJECT
FIRST ANGLE
PROJECTION
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN FIRST QUADRANT
MEANS
ABOVE HP & INFRONT OF VP.
OBJECT IS INBETWEEN
OBSERVER & PLANE.
ACTUAL PATTERN OF
PLANES & VIEWS
IN
FIRST ANGLE METHOD
OF PROJECTIONS
X
Y
VP
HP
PP
FV
LSV
TV

## Slide 21
ACTUAL PATTERN OF
PLANES & VIEWS
OF
THIRD ANGLE PROJECTIONS
X
TV
LSV
FV
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN THIRD QUADRANT
( BELOW HP & BEHIND OF VP. )
PLANES BEING TRANSPERENT
AND INBETWEEN
OBSERVER & OBJECT.
FOR T.V.
FOR S.V.
FOR F.V.
P.P.
V.P.
F.V.
S.V.
OBJECT
Y
THIRD ANGLE
PROJECTION

## Slide 22
FV

## Slide 25
Two dimensions are visible.
What is third dimension?
Another view is required.
Example 1

## Slide 27
Example 2

## Slide 29
Example 2: Reference Line

## Slide 30
Example 2: Reference Line

## Slide 31
If a face is perpendicular to the direction of viewing, its true shape and actual size will be seen in that view.
If a face is parallel to the direction of viewing, it is seen as a line in that view. This view is called the line view or edge view.
If a face is inclined to the direction of viewing, its true shape and size will not be seen in any view.
If an edge of the object is perpendicular to the direction of viewing, its actual length will be seen in that view.
If an edge of the object is parallel to the direction of viewing, it is seen as a point in that view. This view is called point view.
If an edge of the object is inclined to the direction of viewing, its shortened length (projected) will be seen in that view. The shortened length is obtained by locating the end points of the edge.
To obtain the projections of various faces of an object, the following rules must be observed

## Slide 32
Parallel Surfaces
TV
TV

## Slide 33
Inclined Surfaces
h
w
h
w
w
u
u

## Slide 34
Oblique Surfaces

## Slide 35
Curved Surfaces
h
w
u
h
u
u
w

## Slide 36
1. Natural Method: Revolve the object with respect to observer
Methods of Orthogonal Projection
2. Glass box method: The observer moves around the object.
Front view
Right side view
Top view
Right side
view
Top view
play
play
Front
view
Glass box concept

## Slide 37
Glass box : Revolution of the planes of projection
Bottom view
Left side view
Rear view

## Slide 38
Height
Width
Depth
Relative orientation of views
Left side view
Right side view
Bottom view
Top view
Rear view
Front view

## Slide 39
Summary : Problem solving steps
1
2
3
4
Given

## Slide 40
Steps for Orthographic Views
1. Select the necessary views
2. Layout the selected views on a drawing sheet.
3. Complete each selected views.
4. Complete the
dimensions and notes.
45
152
152
64
25~40
Front
Top
Choose a drawing scale
(say 1:1)
Front
Top
y
y
x
x
x
x
y
y
z

## Slide 46: Construction Lines
Construction lines are used to transfer depth information.
O
45o line drawn from point O
Standard multiviews

## Slide 47: Projecting Side Views
Projecting across meter line
Projecting through arcs
Projecting through 45o projectors

## Slide 48
TV
FV
LSV

## Slide 50
Hidden Features:
The features of the object not seen in a particular view are called as hidden features. The hidden features, internal or external, are shown by drawing dashed lines for the edges (or extreme generators in case of cylindrical or conical features) forming the hidden feature in that particular view.
Draw the RHSV of the object It is clear that, in RHSV (i.e., the view in the direction W) the faces B, G and D will not be seen. As these are hidden features, they are shown by dashed lines

## Slide 51
Example
1. Visible
2. Hidden
3. Center

## Slide 52
View selection procedures
1. Orient the object to the best position relative to a glass box.
2. Select the front view.
3. Select adjacent views.

## Slide 53
Suggestions: Orient the object
1. The object should be placed in its natural position.
NO !
2. The orthographic views should represent the true size and true shape of an object (as much as possible).
GOOD

## Slide 54
Suggestions: Select the front view
1. The longest dimension of an object should be presented as a width (in a front view).
Inappropriate
First choice
Good
Second choice
Use more space

## Slide 55
Inappropriate
2. The adjacent views project from the selected front view should be appeared in a natural position.
Suggestions: Select the front view

## Slide 56
3. It has the fewest number of hidden lines.
Good
Inappropriate
Suggestions: Select the front view

## Slide 57
Suggestions: Select an adjacent view
Inappropriate
Inappropriate
1. Choose the view that has the fewest number of hidden lines.

## Slide 58
2. Choose the minimum number of views that can represent the major features of the object.
Necessary
Necessary
Hole’s information is placed on a separated view.
Suggestions: Select an adjacent view
All information is placed
on a single view.

## Slide 59
3. Choose the views that are suitable to a drawing sheet.
Good
Suggestions: Select an adjacent view
Poor
Not enough space
for dimensioning.
Good
Choose another adjacent view.
Change orientation of the
selected views.

## Slide 60
Summary
View selection has 3 steps
Orient
the object
Select
front view
Select
adjacent views

## Slide 61
Object that requires only one-view
Flat (thin) part having a uniform thickness such as a gasket, sheet metal etc.
Adjacent views provide only a
part’s thickness !
1 Thick
Cylindrical-shaped part.
Example

## Slide 62
Repeat !
Infer from CL
Object that requires only one-view
Example
Example
Flat (thin) part having a uniform thickness such as a gasket, sheet metal etc.
Cylindrical-shaped part.

## Slide 63
Identical adjacent view exists.
Repeat !
Object that requires only two-view
The 3rd view has no significant contours of the object.
(provides no additional information)
Example

## Slide 64
Object that requires only two-view
Identical view exists.
Example 1
The 3rd view has no significant contours of the object.
(provides no additional information)

## Slide 65
Object that requires only two-view
Identical view exists.
Example 2
The 3rd view has no significant contours of the object.
(provides no additional information)

## Slide 66
x
y
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
FOR F.V.
FOR S.V.
FOR T.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
F.V.
S.V.
Example-2

## Slide 67
FOR T.V.
FOR S.V.
F.V.
S.V.
ORTHOGRAPHIC PROJECTIONS
FOR F.V.
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example-3

## Slide 68
S.V.
F.V.
FOR T.V.
FOR F.V.
FOR S.V.
ORTHOGRAPHIC PROJECTIONS
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example-4

## Slide 69
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
S.V.
F.V.
FOR T.V.
FOR F.V.
FOR S.V.
ORTHOGRAPHIC PROJECTIONS
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example-5

## Slide 70
S.V.
F.V.
FOR T.V.
FOR F.V.
FOR S.V.
ORTHOGRAPHIC PROJECTIONS
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
Example-6

## Slide 71
Example-7
x
y
FV
35
35
10
TV
30
20
10
40
70
O
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS

## Slide 72
Example-8
SV
TV
y
x
FV
30
30
10
30
10
30
ALL VIEWS IDENTICAL
FOR T.V.
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
14
ORTHOGRAPHIC PROJECTIONS

## Slide 73
x
y
FV
SV
Example-9
TV
10
40
60
60
40
ALL VIEWS IDENTICAL
FOR T.V.
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
15
ORTHOGRAPHIC PROJECTIONS

## Slide 74
FOR T.V.
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
x
y
FV
SV
ALL VIEWS IDENTICAL
40
60
60
40
10
TOP VIEW
Example-10

## Slide 75
O
20 D
30 D
60 D
TV
10
30
50
10
35
FV
X
Y
RECT.
SLOT
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
TOP VIEW
Example-11

## Slide 76
450
X
FV
Y
30
40
TV
30 D
40
40
15
O
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
Example-12

## Slide 77
LSV
Y
25
25
10
50
FV
X
10
10
15
O
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND LSV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
Example-13

## Slide 78
FOR T.V.
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW THREE VIEWS OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
FRONT VIEW
TOP VIEW
L.H.SIDE VIEW
X
Y
Example-14

## Slide 79
40
20
30 SQUARE
20
50
60
30
10
F.V.
S.V.
O
FOR S.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND SV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
FRONT VIEW
L.H.SIDE VIEW
X
Y

## Slide 80
50
80
10
30 D
TV
O
FOR T.V.
FOR F.V.
PICTORIAL PRESENTATION IS GIVEN
DRAW FV AND TV OF THIS OBJECT
BY FIRST ANGLE PROJECTION METHOD
ORTHOGRAPHIC PROJECTIONS
40
10
45
FV
O
X
Y

## Slide 82
Thank You for Patient Hearing