## Slide 1: CE101 Engineering Drawing Lec5: Projection of Planes
Indian Institute of Technology Guwahati
Notes: Today we will discuss about the Modeling and

## Slide 2: Introduction
Plane: Two-dimensional geometrical entity
For practical purpose, a flat face of an object can be treated as plane
Lamina: A plane having limited extent
Plane can be located by
  Three non-collinear points
  A straight line and a point outside it
  Two parallel or intersecting lines
  Traces of lines
Examples:
  Triangular plane, square plane, rectangle plane, pentagonal plane, hexagonal plane, circular plane, semicircular plane etc.

## Slide 3: Positions of Planes
Plane parallel to an RP
  Plane parallel to the HP
  Plane parallel to the VP
Plane inclined to one RP and perpendicular to the other RP
  Plane is inclined to the HP and perpendicular to the VP
  Plane is inclined to the VP and perpendicular to the HP
Plane perpendicular to both the RPs
Plane inclined to both the RPs (Oblique planes)

## Slide 4: Terms Used In Projections of Planes
True Length (TL): The actual length of a plane is called its true length.
Inclination with the HP (θp): It is the true angle that a plane makes with its projection on the HP. It is indicated by θp.
Inclination with the VP (Φp): It is the true angle that a plane makes with its projection on the VP. It is indicated by Φp.
Horizontal Trace (HT): The real or imaginary line of intersection of a plane with the HP is called the horizontal trace of the plane.
Vertical Trace (VT): The real or imaginary line of intersection of a plane with the VP is called the vertical trace of the plane.
Perpendicular Planes: The planes perpendicular to one or both the RPs.
Oblique Planes: Planes inclined to both the RPs
Line View or Edge View: The view of a plane seen as a line.

## Slide 5: Plane Parallel to An RP
FV
T V
For T.V.
Rectangular plane PARALLEL TO HP
VP
a’
d’
c’
b’
HP
a
b
c
d
A regular pentagon ABCDE of side 30 mm is parallel to the VP. The side AB is perpendicular to the HP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
X1
Y1
e’’
a’’
d’’
b’’
c’’
FV
TV

## Slide 6
HP
a1
b1
c1
d1
VP
VP
a’
d’
c’
b’
VP
a’
d’
c’
b’
FV-3
T V-3
For Fv
For Tv
FV-1
T V-1
For F.V.
For T.V.
For T.V.
For F.V.
HP
a
b
c
d
a1’
d1’
c1’
b1’
HP
a1
b1
c1
d1
FV-2
T V-2
CASE OF A RECTANGLE – OBSERVE AND NOTE ALL STEPS.
SURFACE PARALLEL TO HP
PICTORIAL PRESENTATION
SURFACE INCLINED TO HP
PICTORIAL PRESENTATION
ONE SMALL SIDE INCLINED TO VP
PICTORIAL PRESENTATION
ORTHOGRAPHIC
TV-True Shape
FV- Line // to xy
ORTHOGRAPHIC
FV- Inclined to XY
TV- Reduced Shape
ORTHOGRAPHIC
FV- Apparent Shape
TV-Previous Shape
A
B
C

## Slide 7
X
Y
a
b
c
d
a’
b’
c’
d’
a1
b1
c1
d1
a1
b1
c1
d1
a’
b’
d’
c’
c’1
d’1
b’1
a’1
450
300
Problem 1:
Rectangle 30mm and 50mm sides is resting on HP on one small side which is 300 inclined to VP,while the surface of the plane makes 450 inclination with HP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------// to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? ---One small side.
Hence begin with TV, draw rectangle below X-Y
drawing one small side vertical.
Surface // to Hp
Surface inclined to Hp
Side
Inclined
to Vp
Common question

## Slide 8: Plane Inclined to One RP and Perpendicular to Other RP
Problem 2: A regular pentagon ABCDE of side 30 mm is inclined at 45o to the VP and perpendicular to the HP. The side AB is perpendicular to the HP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV
45
a1
b1
c1
e1
d1
a1’
b1’
c1’
d1’
e1’
Stage 1
Stage II
30
Side a’-b’ is
Perpendicular to HP
Projectors from
a’, b’, c’, d’, e’
Projectors from
a1, b1, c1, d1, e1
Point of
intersection

## Slide 9: Plane Inclined to One RP and Perpendicular to Other RP
X
Y
Problem 3: A regular pentagon of 25mm side has one side on the ground. Its plane is inclined at 45º to the HP and perpendicular to the VP. Draw its projections and show its traces
a
b
c
d
e
25
a’e’
b’d’
c’
a’e’
b’d’
c’
a1
b1
c1
d1
e1
45º
Stage 1
Stage 2
One side
On the ground
One side
On the ground

## Slide 10: Plane Inclined to One RP and Perpendicular to Other RP
Problem 4: Draw the projections of a circle of 50 mm diameter having its plane vertical and inclined at 30º to the VP. Its centre is 30 mm above the HP and 20 mm in front of the VP.
X
Y
1’
2’
3’
4’
5’
6’
7’
8’
9’
10’
11’
12’
30
20
1
2, 12
3, 11
4, 10
5, 9
6, 8
7
1
2, 12
3, 11
4, 10
5, 9
6, 8
7
30º
41’
31’
51’
21’
61’
11’
71’
121’
81’
111’
91’
101’
50 Ø
Stage 1
Stage 2

## Slide 11
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? -------- any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
Problem 5:
A regular pentagon of 30 mm sides is resting on HP on one of it’s sides with it’s surface 450 inclined to HP.
Draw it’s projections when the side in HP makes 300 angle with VP
a’
b’
d’
b1
d
c1
a
c’e’
b
c
d1
b’1
a1
e’1
c’1
d’1
a1
b1
c1
d1
d’
a’
b’
c’e’
e1
e1
a’1
X
Y
450
300
e
SURFACE AND SIDE INCLINATIONS
ARE DIRECTLY GIVEN.

## Slide 12: Plane Inclined to Both RPs
Problem 6: A regular pentagon ABCDE of side 30 mm has one of its edges parallel to the VP and inclined at 30o to the HP. The pentagon is inclined at 45o to the VP. Draw the projections of the pentagon. (common question)
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV
45
a1
b1
c1
e1
d1
a1’
b1’
c1’
d1’
e1’
Stage 1
Stage II
30
a2’
b2’
c2’
d2’
e2’
30
a2
b2
c2
d2
e2
Stage III

## Slide 13: Plane Inclined to Both RPs
Problem 7: Draw the projections of a regular hexagon of 25 mm sides, having one of its side in the HP and inclined at 60o to the VP and its surface making an angle of 45º with the HP.
X
Y
a
b
c
d
e
f
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
f1
a1
c1
b1
d1
e1
45º
60º
a1’
b1’
c1’
d1’
e1’
f1’
Stage I: Plane parallel to HP
Stage II: Plane inclined to HP at 45°and ┴ to VP
Stage III: Side on the HP making 60° with the VP.

## Slide 14: Plane Inclined to Both RPs
A square lamina of 50 mm side rests on one of the corners on the HP. The diagonal through that corner makes 30o to the VP. The two sides containing this corner make equal inclination with HP. The surface of the lamina makes 45o to the HP. Draw the TV and FV of the lamina.
50
45
45

## Slide 15: Plane Inclined to Both RPs
Problem 8: A square lamina of 50 mm side rests on one of the corners on the HP. The diagonal through that corner makes 30o to the VP. The two sides containing this corner make equal inclination with HP. The surface of the lamina makes 45o to the HP. Draw the TV and FV of the lamina.
X
Y
45
a
b
c
d
a’
b’, d’
c’
45
a1’
b1’
d1’
c1’
a1
b1
c1
d1
AC diagonal is already inclined at 45o to HP. Find apparent angle.
30
a
c
a1
c1
a2
c2
d2
b2
a2’
d2’
c2’
d2’

## Slide 16: Plane Inclined to Both RPs
Problem 9: A regular pentagon ABCDE of side 30 mm has one of its edges parallel to the VP and inclined at 30o to the HP. The pentagon is inclined at 45o to the VP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
X
Y
a
b
c
e
d
FV
TV
45
a1
b1
c1
e1
d1
a1’
b1’
c1’
d1’
e1’
Stage 1
Stage II
30
a2’
b2’
c2’
d2’
e2’
30
a2
b2
c2
d2
e2
Stage III

## Slide 17
Problem 10:
A 300 – 600 set square of longest side
100 mm long, is in VP and 300 inclined
to HP while it’s surface is 450 inclined
to VP.Draw it’s projections
(Surface & Side inclinations directly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
c1
X
Y
300
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
c
a’1
b’1
c’1
c’
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
Surface // to Vp
Surface inclined to Vp
side inclined to Hp

## Slide 18
c
c1
X
Y
450
a’1
b’1
c’1
a
c
a’
a
b1
b’
b
a1
b
a’1
b’1
c’1
c’
35
10
Problem 11:
A 300 – 600 set square of longest side
100 mm long is in VP and it’s surface
450 inclined to VP. One end of longest
side is 10 mm and other end is 35 mm
above HP. Draw it’s projections
(Surface inclination directly given.
Side inclination indirectly given)
Read problem and answer following questions
1 .Surface inclined to which plane? ------- VP
2. Assumption for initial position? ------// to VP
3. So which view will show True shape? --- FV
4. Which side will be vertical? ------longest side.
Hence begin with FV, draw triangle above X-Y
keeping longest side vertical.
First TWO steps are similar to previous problem.
Note the manner in which side inclination is given.
End A 35 mm above Hp & End B is 10 mm above Hp.
So redraw 2nd Fv as final Fv placing these ends as said.

## Slide 19
Problem 12:
A regular pentagon of 30 mm sides is resting
on HP on one of it’s sides while it’s opposite
vertex (corner) is 30 mm above HP.
Draw projections when side in HP is 300 inclined to VP.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which side will be vertical? --------any side.
Hence begin with TV,draw pentagon below
X-Y line, taking one side vertical.
b’
d’
a’
c’e’
a1
b1
c1
d1
e1
b1
c1
d1
a1
e1
b’1
e’1
c’1
d’1
a’1
X
Y
a’
b’
d’
c’e’
30
a
b
c
d
e
300
SURFACE INCLINATION INDIRECTLY GIVEN
SIDE INCLINATION DIRECTLY GIVEN:
ONLY CHANGE is
the manner in which surface inclination is described:
One side on Hp & it’s opposite corner 30 mm above Hp.
Hence redraw 1st Fv as a 2nd Fv making above arrangement.
Keep a’b’ on xy & d’ 30 mm above xy.

## Slide 20
T L
a
d
c
b
a’
b’
d’
c’
X
Y
a’
b’
d’
c’
a1
b1
d1
c1
a1
b1
d1
c1
450
300
a’1
b’1
c’1
d’1
a1
b1
d1
c1
a
d
c
b
a’
b’
d’
c’
a’
b’
d’
c’
a1
b1
d1
c1
300
a’1
b’1
c’1
d’1
Problem 13: A circle of 50 mm diameter is
resting on Hp on end A of it’s diameter AC
which is 300 inclined to Hp while it’s Tv
is 450 inclined to Vp.Draw it’s projections.
Problem 9: A circle of 50 mm diameter is
resting on Hp on end A of it’s diameter AC
which is 300 inclined to Hp while it makes
300 inclined to Vp. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AC
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y
The difference in these two problems is in step 3 only.
In problem no.13 inclination of Tv of that AC is
given,It could be drawn directly as shown in 3rd step.
While in no.9 angle of AC itself i.e. it’s TL, is
given. Hence here angle of TL is taken,locus of c1
Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed.Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.

## Slide 21
Problem 14: End A of diameter AB of a circle is in HP
and end B is in VP.Diameter AB, 50 mm long is
300 & 600 inclined to HP & VP respectively.
Draw projections of circle.
The problem is similar to previous problem of circle – no.9.
But in the 3rd step there is one more change.
Like 9th problem True Length inclination of dia.AB is definitely expected
but if you carefully note - the the SUM of it’s inclinations with HP & VP is 900.
Means Line AB lies in a Profile Plane.
Hence it’s both Tv & Fv must arrive on one single projector.
So do the construction accordingly AND note the case carefully..
SOLVE SEPARATELY
ON DRAWING SHEET
GIVING NAMES TO VARIOUS
POINTS AS USUAL,
AS THE CASE IS IMPORTANT
TL
X
Y
300
600
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AB
Hence begin with TV,draw CIRCLE below
X-Y line, taking DIA. AB // to X-Y

## Slide 22
As 3rd step
redraw 2nd Tv keeping
side DE on xy line.
Because it is in VP
as said in problem.
X
Y
a
b
c
d
e
f
Problem 15:
A hexagonal lamina has its one side in HP and
Its apposite parallel side is 25mm above Hp and
In Vp. Draw it’s projections.
Take side of hexagon 30 mm long.
ONLY CHANGE is the manner in which surface inclination
is described:
One side on Hp & it’s opposite side 25 mm above Hp.
Hence redraw 1st Fv as a 2nd Fv making above arrangement.
Keep a’b’ on xy & d’e’ 25 mm above xy.
25
f’
e’
d’
c’
b’
a’
f’
e’
d’
c’
b’
a’
a1
b1
c1
d1
e1
f1
c1’
b’1
a’1
f’1
d’1
e’1
f1
a1
c1
b1
d1
e1
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diameter horizontal? ---------- AC
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y

## Slide 23
350
400
a’
b’1
c’1
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
c1
d1
b’
c’
a’1
d’1
d1
b1
c1
a1
X
Y
300
b’1
c’1
c1
a’1
d’1
d1
b1
c1
a1
350
a’
d’
a’
b’
d’
c’
a
c
b
d
a1
b1
d1
b’
c’
X
Y
TL
Problem 6: A rhombus of diagonals 40 mm and 70 mm long respectively has one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP. If the top-view of the same diagonal makes 400 inclination with VP, draw it’s projections.
Problem 7: A rhombus of diagonals 40 mm and 70 mm long respectively having one end of it’s longer diagonal in HP while that diagonal is 350 inclined to HP and makes 300 inclination with VP. Draw it’s projections.
Read problem and answer following questions
1. Surface inclined to which plane? ------- HP
2. Assumption for initial position? ------ // to HP
3. So which view will show True shape? --- TV
4. Which diagonal horizontal? ---------- Longer
Hence begin with TV,draw rhombus below
X-Y line, taking longer diagonal // to X-Y
c2
The difference in these two problems is in step 3 only.
In problem no.6 inclination of Tv of that diagonal is
given,It could be drawn directly as shown in 3rd step.
While in no.7 angle of diagonal itself I.e. it’s TL, is
given. Hence here angle of TL is taken,locus of c1
Is drawn and then LTV I.e. a1 c1 is marked and
final TV was completed.Study illustration carefully.
Note the difference in
construction of 3rd step
in both solutions.

## Slide 24: Auxiliary Plane Projection Method
X
Y
Prroblem 16: A regular pentagon ABCDE of side 30 mm has one of its edges parallel to the VP and inclined at 30o to the HP. The pentagon is inclined at 45o to the VP. Draw the projections of the pentagon.
a’
b’
c’
d’
e’
a, b
c, e
d
45
X1Y1
b1’
a1’
d1’
c1’
e1’
30
X2Y2
Distance of a, b, c, d, e from X1Y1
a2
b2
c2
e2
d2
Pentagon is parallel to VP and perpendicular to HP
Distance of a’, b’, c’, d’, e’ from XY
Pentagon is inclined at 45o to VP
Side AB is inclined at 30o to HP

## Slide 25
Thank You for Patient Hearing